## Slide 1: CIBC 5022 Contouring
Contouring
An imaginary line on the ground surface joining the points of equal elevation is known as a contour.
Contour map: A map showing contour lines is known as a contour map
A contour map gives an idea of the surface features as well as their relative positions in plan which serves the purpose of both a plan and section
Notes: A contour line is a line in which the ground surface is intersected by a level surface obtained by joining points of equal elevation. This line on the map represents a contour and is called a contour line.

## Slide 5: Level
Notes: A level essentially
comprises a telescope
rotatable about a vertical
axis; it is used to create
a horizontal line of sight
so that height differences
can be determined
and stakeouts can be
performed.

## Slide 6: The Total Station
Notes: A total station consists of a
theodolite with a built-in
distance meter (distancer),
and so it can measure
angles and distances at the
same time. Today’s
electronic total stations all
have an opto-electronic
distance meter (EDM) and
electronic angle scanning.
The coded scales of the
horizontal and vertical
circles are scanned
electronically, and then the
angles and distances are
displayed digitally. The
horizontal distance, the
height difference and the
coordinates are calculated
automatically and all
measurements and
additional information can
be recorded.

## Slide 7: Setting up the instrument
Notes: 1.Extend the legs of the
tripod as far as is
required and tighten the
screws firmly.
2. Set up the tripod so that
the tripod plate is as
horizontal as possible
and the legs of the
tripod are firm in the
ground.
3. Now, and only now,
place the instrument on
the tripod and secure it
with the central fixing
screw.
After setting up the
instrument, level it up
approximately with the
bull’s-eye bubble.
Turn two of the footscrews
together in opposite
directions. The index finger
of your right hand indicates
the direction in which the
bubble should move
(illustration, top right).
Now use the third footscrew
to centre the bubble
(illustration, bottom right).
To check, rotate the instrument
180°. Afterwards, the
bubble should remain
within the setting circle. If it
does not, then readjustment
is required (refer to the user
manual).
For a level, the compensator
automatically takes
care of the final levellingup.
The compensator
consists basically of a
thread-suspended mirror
that directs the horizontal
light beam to the centre of
the crosshair even if there
is residual tilt in the telescope
(illustration, bottom).
If now you lightly tap a leg
of the tripod, then (provided
the bull’s-eye bubble
is centred) you will see how
the line of sight swings
about the staff reading and
always steadies at the
same point. This is the
way to test whether or not
the compensator can swing
freely.

## Slide 8: Setting up profiles
Notes: During building alignment,
it is useful to extrapolate
the sides of the building to
beyond the limits of the excavation
and there to erect
profile boards on which the
extensions are marked
exactly by hammering in
nails. These can be connected
to strings or wires at
any time during the construction
sequence, indicating
the required
positions of the walls.
In the following example,
profile boards are to be
erected parallel to the proposed
walls of a large
building and at distances of
a and b respectively from
the boundaries (illustration,
left).
1.Establish a baseline AB
parallel to the left-hand
boundary and at a freelyselectable
distance c.
2.Mark the point A at the
defined distance d from
the upper boundary; it
will be the first location
for the total station.
3.Using a boning rod, mark
the point B at the end of
the baseline.
4.Set up the total station on
point A, target point B,
and set out the points A1,
A2 and A3 in this alignment
in accordance with
the planned length of the
side of the building.
5.With point B sighted, set
the horizontal circle to
zero, turn the total station
by 100 gon (90°) and set
out the second line AC
with the points A4, A5
and A6.
6.The points on the profile
boards are then set out
in a similar manner,
starting from the points
A1 to A6 respectively.
If the foundations have not
yet been excavated, you
can set out the sides H1H2
and H1H3 of the building
directly and use them as
the starting line for
marking the points on the
profile boards.
For smaller buildings it is
easier to set out the profile
boards using an optical
square (right-angle prism)
and a measuring tape.

## Slide 9: Contouring
Notes: (a) Method of squares,
(b) Method of cross-section, or
(c) Radial line method.
Method of Squares: In this method area is divided into a number of squares and all grid points are marked (Ref. Fig. 1).
Fig. 1
Commonly used size of square varies from 5 m × 5 m to 20 m × 20 m. Levels of all grid points are established by levelling. Then grid square is plotted on the drawing sheet. Reduced levels of grid points marked and contour lines are drawn by interpolion [Ref. Fig. 1].
Method of Cross-section: In this method cross-sectional points are taken at regular interval. By levelling the reduced level of all those points are established. The points are marked on the drawing sheets, their reduced levels (RL) are marked and contour lines interpolated.
Fig. 2
Figure 2 shows a typical planning of this work. The spacing of cross-section depends upon the nature of the ground, scale of the map and the contour interval required. It varies from 20 m to 100 m. Closer intervals are required if ground level varies abruptly. The cross- sectional line need not be always be at right angles to the main line. This method is ideally suited for road and railway projects.
Radial Line Method: [Fig. 3]. In this method several radial lines are taken from a point in the area. The direction of each line is noted. On these lines at selected distances points are marked and levels determined. This method is ideally suited for hilly areas. In this survey theodolite with tacheometry facility is commonly used.