## Slide 1: Lesson 2 Construction Levelling 1 Lecture
CIBC5022 Site Survey Preparation and Analysis
Notes: No Use of big plans this week. Crap Drainage plans.

## Slide 2
Demonstrate knowledge of principles related to provision of services for small, medium and large buildings.
Explain purposes and operating principles of building services;
Explain principles of coordination and placement and reticulation of services;
Demonstrate a knowledge of legislative requirements relevant to services.
Course Aim
To enable the student to develop the skills and knowledge to assist and conduct site surveys and analysis

## Slide 3
Learning outcomes
Learning Outcomes • Describe site survey preparation and set out • Discuss and review information for contour plan preparation • Generate graphical communications relevant to construction
Indicative curriculum (May include but are not limited to)
Curriculum
• Overview of types – boundary
• Site plan preparation
• Survey instruments
• Measurements
• Contour plan preparation
• Graphical communication

## Slide 4
Levelling Instrument Parts
.

## Slide 5
Definitions
1. Datum
An or plane to which levels are referred. Usually tarbitrary horizontal line aken as 10.00 or 100.00. (On most commercial jobs, the mean sea level is the reference point.)
2. Temporary Bench mark
A levelling reference point established in a position adjacent to or on the site to provide a convenient reference to the datum. This may in fact be the datum.
3. Bench mark
Established by Lands and Survey Department, Councils, Registered Surveyors, Engineers. These are recorded at certain points as Above Mean Sea Level (AMSL).
4. Reduced level
Levels expressed in terms of the datum, may be indicated by;
(a) Spot levels on the plan e.g. 103.420, 96.820,
(b) Vertical section,
Contour lines.
To avoid negative reduced levels, the datum will have to be set well below the lowest level being worked on.

## Slide 6
Definitions (Continued)
5. Line of collimation Horizontal line of sight through the telescope of the instrument
6. Station point Position of the instrument when taking spot levels.
7. Back sight (BS) The first sight taken after the instrument is set up or moved and re-setup.
8. Fore sight (FS) The last sight taken before the instrument is moved.
9. Intermediate sight (IS) Any sight between fore sight and back sight.
10. Change station
Change point of the instrument, the point at which the fore sight of one collimation line is linked to the back sight of the next collimation line.
11. Stadia lines
Two short level lines equal distance above and below the levelling line in the telescope. The distance between the stadias is read off the staff. Distance between stadia lines multiplied by 100 = distance from instrument to staff.

## Slide 7
The automatic level uses a prism that is hung in a variety of ways but can always assume a vertical axis from its point of suspension.
The prism and sighting mechanism are arranged so that when the pendulum is vertical, the instrument is automatically levelled. The pendulum is unlocked when the instrument is within 5 degrees of the horizontal.
The Level needs to be set up so that the base upon which it sits, the tripod, must be level.
Essentially Levelling is now a height difference between two points
The basic principle of levelling involves determining the height difference between two points.
The height difference is calculated from the difference between the two staff readings for the points A and B respectively.
Setting Up The Level Anywhere

## Slide 8
Levelling The Instrument
Extend the legs of the tripod as far as is required and tighten the screws firmly.
Set up the tripod so that the tripod plate is as horizontal as possible and the legs of the tripod are firm in the ground.
Push two legs of the tripod firmly into the ground.
Get tripod head approximately level and push third leg into the ground. Do not set the tripod too low!
If the tripod is set on a steep slope, two of the legs must be secured in the ground roughly at the same height on the downhill side of the instrument.
The remaining leg is secured to the uphill side. Adjust the remaining leg to level the tripod head by sliding leg adjustment
Now, and only now, place the instrument on the tripod and secure it with the central fixing screw

## Slide 9
After setting up the instrument, level it up approximately with the bull’s-eye bubble.
Attach the levelling instrument firmly to the tripod head. If the setting up bubble is circular, the bubble must be in the centre of the ring.
Move the bubble towards the centre direction by using screws 1 and 2 to level the bubble. That is, turn two of the footscrews (of the levelling instrument), together in opposite directions.
The index finger of your right hand indicates the direction in which the bubble should move(illustration, top right)

## Slide 10
Compensator
.
Now use the third footscrew to centre the bubble (illustration, bottom right). That is, move the third screw to centralise the bubble. Once the bubble is centralised, check to ensure the instrument is levelled by rotating the instrument at 180 degrees and 360 degrees. If the bubble remains within the circle the instrument is correctly set. (Note: not necessary for automatic levels)
For a level, the compensator automatically takes care of the final levelling-up
The compensator consists basically of a thread-suspended mirror that directs the horizontal light beam to the centre of the crosshair even if there is residual tilt in the tele-scope (illustration, bottom).
If now you lightly tap a leg of the tripod, then (pro-vided the bull’s-eye bubble is centred) you will see how the line of sight swings about the staff reading and always steadies at the same point. This is the way to test whether or not the compensator can swing freely.

## Slide 11
Measuring distances optically with the level
The reticle carries two stadia lines arranged symmetrically to the crosshair.
Their spacing is such that the distance can be derived by multiplying the corresponding staff section by 100. (This diagram is a schematic representation).
Accuracy of the distance measurement: From 10 – To 30 cm
Using the Stadia to Measure Distance Between Stations
Note; The degree of accuracy for stadia is 100 mm in 30 metres

## Slide 12
Levelling Staff
Standard staffs are 3 metres, 4 metres, or 5 metres long, they fold or telescope down to about1200 mm, have a reading face at least 38 mm wide.
The staff is graduated in 10mm increments with alternating black and red figures per metre on a white staff.
Reading the staff to the graduation will give 0.01m accuracy. If three decimal places of accuracy are needed, it has to be estimated.

## Slide 13
The Reticle
STADIA LINES (view through telescope)

## Slide 14
Line Levelling – Taking a Reading
The method of taking readings differs slightly with the type of instrument being used; however the instrument must be set up level.
The staff holder must hold the staff on the mark or peg.
Ensure the staff is plumb and facing the instrument.
Ensure the staff is visible for the instrument to focus on. If the parallax has been eliminated, the black hair line will be sharply outlined against the staff.
To remove the parallax you will need to focus the cross hairs separately.
This is done by having the background out of focus and then focusing the cross hairs against the out of focus background.

## Slide 15
Line Levelling
If the points A and B are widely separated, the height difference between them is determined by line levelling with target distances generally between 30 and 50 metres.
Pace out the distances between the instrument and the two staffs; they need to be about the same
Set up the instrument at S1.
Set up the staff precisely vertically at point B; read off and record the height (back sight R).
Set up the staff at the turning point 1 (ground plate or prominent ground point); read off and record the height (foresight V).

## Slide 16
Levelling Check (Cont’d)
Then set up the instrument at S2 (the staff remains at the turning point 1).
Carefully rotate the staff at the turning point 1 so that it faces the instrument.
Read off the back sight and continue.
The height difference between A and B is equal to the sum of the back sight and the foresight.

## Slide 17
Levelling in an Excavation
Occasions arise where you need to check levels or calculate the differences between levels.

## Slide 18
Excavation Levelling
Say, in an excavation, a point B is to be set out at a height ∆H = 1.00 metre below street level (Point A).
Set up the level so that the sighting distances to A and B are about the same.
Set up the staff at A and read off the backsight R = 1.305.
Set up the staff at B and read off the foresight V = 2.520.The difference h from the required height at B is calculated as: h = V – R - ∆H = 2.520 –1.305 – 1.00 = +0.215m
4. Drive in a post at B and mark the required height (0.215m above ground level).

## Slide 19
Topography Levelling Levelling
In another frequently-used method involving the topography or actual ground level
1. the required staff reading is calculated in advance: V= R - ∆H = 1.305 - (-1.000) = 2.305
2. The levelling staff is then moved upwards or down-wards until the required value can be read off between A and the the moving staff at B until the required reading is obtained.
3. Then a stake is hammered in at B and its level is again recorded.

## Slide 20
Setting Out Roads
Longitudinal and transverse profiles form the basis for the detailed planning and stakeout of communications routes (e.g. roads) and also for the calculation of fill and for the best possible accommodation of the routes to the topography

## Slide 21
Another Line Levelling Method - Roads
.
First of all the longitudinal axis (road-line) is staked out and stationed; this means that points are established and marked at regular intervals. A longitudinal profile is then created along the roadline, the heights of the station points being deter-mined by line levelling. (See top diagramme of Longitudinal Levelling)
At the station points and at prominent topographic features, transverse profiles (at right-angles to the roadline) are then recorded. The ground heights for the points in the transverse profile are determined with the aid of the known Instrument height. First, position the staff at a known station point; the instrument height comprises the sum of the staff reading and the station point height

## Slide 22
Measuring With The Level
Now subtract the staff readings (at the points on the transverse profile) from the instrument height; this gives the heights of the points involved.
The distances from the station point to the various points in the transverse profiles are determined either with the surveyor’s tape or optically using the level.
When representing a longitudinal profile graphically, the heights of the station points are expressed at a much bigger scale (e.g. 10x greater) than that of the stationing of the longi-tudinal direction, which is related to a round reference height (illustration above).

## Slide 23
Taking Spot Levels – Rise and Fall Method
This method of taking levels is more suited for taking levels around a proposed building to calculate excavations
Set up the instrument in a position where most spots can be seen.
Ensure instrument is levelled accurately.
Focus the cross hairs in the telescope (at start of levelling only).
Focus the telescope until staff readings are clear.
Read, record, and check the readings required (Level, or stadia and level). Do not hold the instrument while taking the readings.
6. Signal staff holder to move to next spot and repeat steps 4, 5, and 6. Ensure that staff is held plumb while taking the readings. Booking and reducing the readings Rise and Fall method.

## Slide 24
Levels – Rise and Fall Method
• Record BS, IS, FS, readings in the correct columns as you take the readings.
• When readings are complete, calculate rises & falls
• Calculate reduced levels.
• Check your calculations.
• Example shown over the page

## Slide 25
Rise and Fall Method - Example

## Slide 26
Levels – Methodology
1. To calculate the rise or fall Subtract the second reading from the first reading. If the answer is positive, there is a rise. If the answer is negative (-), there is a fall.
2. Calculate the reduced level (RL) by adding rises and deducting falls from the previous RL reading. To check on rise and fall method
a. Add back sights, add fore sights.
o Take total of fore sights from total of back sights (or vice versa).
b. Add rises, add falls.
o Take total of rises from total of falls (or vice versa).
c. Subtract last reduced level reading from first reduced level reading (or vice versa).
3. Answers from (a) (b) and (c) should be equal

## Slide 27
Levels – Rise and Fall Method

## Slide 28
Levels – Rise and Fall Method

## Slide 29
Content Title
n new levels, the com-pensator has been adjusted at room temperature, so that the line of sight is hori-zontal even if the instru-ment is tilted slightly. This situation changes if the temperature fluctuates by more than ten or fifteen degrees, after a long jour-ney, or if the instrument is subjected to strong vibra-tion. It is then advisable to inspect the line of sight, particularly if more than one target distance is being used.

## Slide 30
Levelling Check
.
In flat terrain, set up two staffs not more than 30 metres apart.
Set up the instrument so that it is equidistant from the two staffs (itis enough to pace out the distance)
Read off from both staffs and calculate the height difference (illustration above).Staff reading A = 1.549 Staff reading B = 1.404 ∆H = A – B = 0.145
Set up the instrument about one metre in front of staff A and take the staff reading (illustration below).Staff reading A = 1.496
Calculate the required reading B:Staff reading A = 1.496 – ΔH = 0.145
Required reading B = 1.351
Take the staff reading B
If it differs from the required reading by more than 3mm, adjust the line of sight (refer to instruction manual).

## Slide 31
THE END