## Slide 1
Climate Change and Urban Design
Matthew Bradbury
Xinxin Wang
Notes: What I want to do in this talk is talk about what th environmental effects of Climate change in particular sudden unpredictable downfall on the way we will live and design our cities . This talk isn’t going to be about the science of climate change or policy or ways in which these effects can be mitigated rather I’m looking at the way we actually design our cities, the shape the form the planning of a city and how that can actually help us to build resilience to the effects of climate change but equally can actively endanger our citizen,
So I should so the if we follow this particular line of argument then the answer is going to appear somewhat heretical especially to some of the excepted Urban design mores( mor rais).
PROBLEM
We all understands the the problem of urban storm water , the contamination of the receiving environs and when we get to much the overwhelming of the stormwater infrastructure leading to flooding

## Slide 11: New Urban Form
To help address these environmental problems, a new urban form that accommodates the remediation of these difficulties in an inclusive and encompassing way will have to be found. The first step in building urban resilience is to understand that the environmental problems of climate change are not simply isolated incidents, such as occasional flooding events, but part of larger connected environmental systems. Once this is understood then a linked strategy that places the design of the urban master plan at the heart of the environmental remediation process, rather than a series of small haphazard interventions, becomes possible.

## Slide 12
Building urban resilience to the effects of climate change means that an understanding of ecological systems in the city is necessary to address the problems. Engaging with the ecology of the urban development site, not as a fixed system but as a fluid set of environmental conditions, will help to both understand and address the dynamic effects of climate change.

## Slide 13
The process starts with the development site being placed into the catchment and an environmental audit of the conditions is made.
Identifying and protecting the existing hydrological structure of the catchment is important, and this can be done by using GIS to identify catchments, overland flow path and riparian margins.
Mapping these corridors enables them to be protected from development pressures. The ability of a city to absorb rainfall by becoming more pervious is also critical.

## Slide 14
Making the city form more open and the building programme more compact by clustering building together are ways to achieve this goal.
These two broad strategies, identifying and protecting existing riparian corridors and making the city more open and absorbent, can help the catchment to become more responsive to the impact of climate change.

## Slide 15
By placing a development site within a hydrological catchment, which can be part of an existing city or a greenfield site, the environmental impact of the climate change on the catchment and therefore the urban form of the development site can be understood.

## Slide 16: 1 Protect and Enhance Natural Spaces
By protecting and, where necessary, restoring natural spaces within the catchment, the ability to deal with environmental problems such as littoral and pluvial flooding is increased.

## Slide 17: 2 Restore/Enable/Protect Biodiversity
Restoring, enabling and protecting indigenous terrestrial and aquatic biodiversity is critical to ensuring the continuing ecological health of a catchment. This can be helped by protecting any existing indigenous ecotones and indigenous habitats. If damaged ecotones or/and indigenous habitats can be identified within the catchment, then prioritising the restoration by replanting on sensitive slopes, riparian corridors and ridges is important.

## Slide 18: 3 Protect Riparian Margins
Protection of riparian margins is critical to the protection of stream networks. This goal can be accomplished with the indigenous planting of high biomass species in a buffer zone around the stream. This method helps to increase aquatic and terrestrial biodiversity within the riparian corridors. In addition to riparian corridors, wetland and flood detention areas should also be protected by planning a buffer area around these zones. By protecting the areas around urban streams through the replanting of indigenous species, erosion can be reduced, sediment trapped, and phosphorus, nitrogen, and other contaminants present in urban run-off can be filtered before reaching the stream, protecting and enhancing both aquatic and terrestrial wildlife habitats (Wenger & Fowler, 2000)

## Slide 19: 4 Reduce Impervious Surfaces
Reducing the percentage of impervious surfaces within the catchment helps to reduce amount of stormwater run-off (M. van Roon & Moore, 2004). Van Roon qualifies this technique further by defining an ‘effective impervious’ surface as being an impervious area that drains directly into a waterway. This can mean an impervious surface directly adjacent to a waterway, or an impervious surface that is linked to a waterway via a piped system

## Slide 20: 5 New Urban Form Through Clustering
Conventional housing development models usually assume that the building and associated infrastructure will cover most of the site irrespective of any areas of environmental vulnerability, such as overland flow paths or native bush fragments. area allocated as being the least environmentally sensitive is critical. How is the amount of building required to fulfil the real estate criteria to make a profitable development able to be accommodated on a site that will almost inevitably be smaller than the normal development model requires? Van Roon points to the use of clustering as a building technique that can accomplish this task. Clustering the building programme will maintain and help to restore the existing hydrological network within the catchment.

## Slide 21
Design Process
Define the area and hydrological characteristics of the catchment such as overland flow paths with GIS mapping
Determine the the permeable / impermeable surface ratio of the catchment
Use the Rational Method to help calculate the amount of water in a catchment
Adjust the building density using the Floor Area ratio to increase the amount of pervious surface

## Slide 22: GIS Mapping
http://file.scirp.org/Html/8-6701908/8554f1ba-22a4-4abe-ac4f-16b82ffa82e0.jpg

## Slide 25: Impervious pervious surface ratio
http://www.mass.gov/anf/images/itd/massgis/datalayers/imp-surf.png

## Slide 27: Density : FAR
Reduce the building footprint

## Slide 28: WHENUAPAI
Auckland New Zealand is expanding with expected increase in population by one million people. One of the areas that will accommodate this expansion is Whenuapai in West Auckland on the Waitamata harbour. The planned development proposes a roughly radial grid plan with three bands of housing density; from low-density areas at the waters edge to medium density in the centre to high density at the periphery. Using GIS analysis reveals a number of important stream corridors that link the hinterland to the coast. Turning the existing streams into a new park system makes an ecologically connected network. To compensate for the lost of buildable section denser living zones are planned at the waters edge, around the mouth of the streams.
The results are; rainfall absorption is increased, a new park system is created, and the more people get the opportunity of enjoying living on the coast in apartments.

## Slide 34
海绵城市 - 弗努阿派 - 场地分析 - 等高线

## Slide 37
海绵城市 - 弗努阿派 – 汇水区

## Slide 40
海绵城市 - 弗努阿派 – 汇水区 – 100米缓冲区