## Slide 1: CIBC 5022 Surveying Equipment
Lesson objectives
  Identify common survey apparatus and uses

## Slide 2: Fibreglass Tape
Notes: Lengths of 50', 100', 200, and 300' common. Tape maybe graduated in feet and inches, feet and 1/100', or metric.

## Slide 3: Steel Tape
Notes: It should be cleaned after using and kept free from rust.

## Slide 4: Measuring Wheel
Notes: Used to measure long distances such as field boundaries or road length where high accuracy is not required.

## Slide 5: Line Level
Notes: It consists of a bubble tube housedin a metal or plastic case which has hooks for attaching to the line.

## Slide 6: Plumb Bob
Notes: It can also be used to establish a plumb line in laying brick or concrete blocks. Also used to establish a survey instrument (like a transit) above a specific point.

## Slide 7: Chalk Line
Notes: A special container contains the chalk powder and line which is on a winding spool.

## Slide 8: Direct Elevation Rod
Notes: Rod reads elevations directly (without subtraction from the HI) by used a sliding tape. Some rods have a cut/fill scale for use in grading.

## Slide 9: Global Position System Receiver
Notes: Commonly called GPS receivers, they used satellites to establish the user’s position (e.g., latitude and longitude). Recreational receivers have an accuracy of 13 m and survey grade receivers have an accuracy of 2 cm. Differential GPS receivers (accuracy 2cm – 1 m) are commonly used in agriculture to map field boundaries, scout fields, and provide tractor guidance.

## Slide 10: Laser Level
Notes: A level that used a rotating laser beam to establish a level plane. Leveling can be done with a single person.

## Slide 11: Range pole
Notes: A simple pole used in lieu of a rod where elevation measurement is not needed.

## Slide 12: Philadelphia Rod
Notes: Reads like a tape measure. An adjustable target is available to allow readings up to 700 feet in distance.

## Slide 13: Laser Level Receiver
Notes: The receiver that detects the laser beam of the laser level. Can be fitted to a Philadelphia or Direct Elevation rod.

## Slide 14: Transit
Notes: Similar to a level, but a transit telescope can be tilted vertically to measure vertical angles. Surveyor’s have generally replaced these with "Total Stations", but transits are still used to measure vertical angles in construction.
Transit is the most universal of surveying
instruments – primary use is for measurement
or layout of horizontal and vertical angles – also
used to determine vertical and horizontal
distance by stadia, prolonging straight lines,
and low-order leveling

## Slide 15: Surveying Tripod
Notes: Used to hold a level or other survey instrument. To protect threads, keep cap on when not in use.

## Slide 16: Builder's Level
Notes: A telescope instrument used to check level of forms or field grades. Builders' levels are designed to be used for short distances. Farm or dumpy levels are similar to builder's levels, but have more powerful telescopes. Farm levels are used for longer distances. Both instruments are leveled manually using adjusting screws. An "auto" level requires less manual leveling and has only three leveling screws.

## Slide 17: Builder's Level
Notes: A telescope instrument used to check level of forms or field grades. Builders' levels are designed to be used for short distances. Farm or dumpy levels are similar to builder's levels, but have more powerful telescopes. Farm levels are used for longer distances. Both instruments are leveled manually using adjusting screws. An "auto" level requires less manual leveling and has only three leveling screws.
Automatic level.
The automatic level uses a prism that is hung in a variety of ways but can always assume a
vertical axis from its point of suspension. The prism and sighting mechanism are arranged
so that when the pendulum is vertical, the instrument is automatically levelled. The
pendulum is unlocked when the instrument is within 50 of the horizontal. (See Sokkia
product sheet)
Levelling Staff
Standard staffs are 3 metres, 4 metres, or 5 metres long, they fold or telescope down to
about1200 mm, have a reading face at least 38 mm wide. The staff is graduated in 10mm
increments with alternating black and red figures per metre on a white staff. Reading the
staff to the graduation will give 0.01m accuracy. If three decimal places of accuracy are
needed, it has to be estimated.

## Slide 18: Levelling Terms
Datum
Temporary Bench mark
Bench mark
Reduced level
Line of collimation
Horizontal line of sight through the telescope of the instrument
Station point
Back sight (BS)
Fore sight (FS)
Intermediate sight (IS)
Change station
Stadia lines
Two short level lines equal distance above and below the levelling line in the telescope.
Notes: Levelling Terms
Datum
An arbitrary horizontal line or plane to which levels are referred. Usually taken as 10.00 or
100.00. (On most commercial jobs, the mean sea level is the reference point.)
Temporary Bench mark
A levelling reference point established in a position adjacent to or on the site to provide a
convenient reference to the datum. This may in fact be the datum.
Bench mark
Established by Lands and Survey Department, Councils, Registered Surveyors, Engineers.
These are recorded at certain points as Above Mean Sea Level (AMSL).
Reduced level
Levels expressed in terms of the datum, may be indicated by
(a) Spot levels on the plan e.g. 103.420, 96.820,
(b) Vertical section,
(c) Contour lines.
To avoid negative reduced levels, the datum will have to be set well below the lowest level
being worked on.
Line of collimation
Horizontal line of sight through the telescope of the instrument
Station point
Position of the instrument when taking spot levels.
Back sight (BS)
The first sight taken after the instrument is set up or moved and re-setup.
Fore sight (FS)
The last sight taken before the instrument is moved.
Intermediate sight (IS)
Any sight between fore sight and back sight.
Change station
Change point of the instrument, the point at which the fore sight of one collimation line is
linked to the back sight of the next collimation line.
7
Stadia lines
Two short level lines equal distance above and below the levelling line in the telescope.
The distance between the stadias is read off the staff. Distance between stadia lines
multiplied by 100 = distance from instrument to staff.

## Slide 19: Theodolite
A theodolite is a precision optical instrument for measuring angles between designated visible points in the horizontal and vertical planes
Notes: THEODOLITE
The theodolite is used to measure horizontal and
vertical angles for exact survey work
Compared to transit, theodolite are:
Compact
Lightweight
More accuracy and precise
Transits are more common in the U.S. but are being
replaced by theodolite
TYPE OF THEODOLITE
Repaeting theodolite
Directional Theodolite
Electrical Digital Theodolite
Total Station
Circles can be instantaneously zeroed, or initialized to any value
Angles can be measured with increasing values either left or
right
Angles measured by repetition can be added to provide a total
larger than 360°
Mistakes in reading angles are greatly reduced
Speed of operation is increased
Cost of instrument is lower

## Slide 20: Theodolite

## Slide 21: Total Station
Notes: TOTAL STATION
A Total Station integrates the functions of a theodolite for
measuring angles, an EDM for measuring distances, digital data
and information recording. Examples of Total Stations are the
Nikon DTM 801, Topcon and Geodimeter 400 series
Examples of usage
General purpose angle and distance measurements.
Provision of control surveys, Contour and detail mapping,
setting out and construction work
Factors which influence the use of Total Stations
A clear line of sight between the instrument and the
measured points is essential
A well defined measurement point or target/prism is
required to obtain the maximum accuracy
TOTAL STATION INSTRUMENT
An electronic digital theodolite and an electronic distance
measurement in one integral unit
They can automatically record horizontal and vertical angles
and slope distances from a single setup
Slope distance can be reduced to horizontal and vertical
components instantaneously
Given initial data they will display positions and elevations of
sighted points

## Slide 22: Total Station Cababilities
Volume Calculations
Area Calculations
Remote Heights
Tie Distances
Notes: Volume Calculations lets you measure surface points and boundaries, then computes volume from those measurements
Area Calculations allows you to set up a total station within view of the entire survey area, measures a sequence of points clockwise around the area, then calculates the area from that data.
Remote Heights lets you measure inaccessible high points. Place a reflector anywhere below the height you want to measure, enter the reflector height, target it, measure the distance, and then target the high point. The total station calculates the height difference between the ground and high points.
Tie Distances calculates the distance and height differences between two points. Set up your total station anywhere, measure the distances to points A and B, and the total station calculates both distance D and height difference H. You can also store points in memory to calculate tie distance and height difference.