## Slide 1
Lecture 12
Graphical Interface
(Using The Builder's Level)
CIBC5022 Site Survey Preparation and Analysis May 30th 2022
Rodney Harvey Unitec Lecturer

## Slide 2: Levelling Terms
Datum
An arbitrary horizontal line or plane to which levels are referred. Usually taken as 10.00 or 100.00. (On most commercial jobs, the mean sea level is the reference point.)
Temporary Bench mark
A levelling reference point established in a position adjacent to or on the site to provide a convenient reference to the datum. This may in fact be the datum. Bench mark
Established by Lands and Survey Department, Councils, Registered Surveyors, Engineers. These are recorded at certain points as Above Mean Sea Level (AMSL).

## Slide 3
Reduced level
Levels expressed in terms of the datum, may be indicated by
Spot levels on the plan e.g. 103.420, 96.820,
Vertical section,
Contour lines.
To avoid negative reduced levels, the datum will have to be set well below the lowest level
being worked on.
Line of collimation
Horizontal line of sight through the telescope of the instrument
Station point
Position of the instrument when taking spot levels.

## Slide 4
Back sight (BS)
The first sight taken after the instrument is set up or moved and re-setup.
Fore sight (FS)
The last sight taken before the instrument is moved.
Intermediate sight (IS)
Any sight between fore sight and back sight.

## Slide 5: Levelling and Booking
Change station
Change point of the instrument, the point at which the fore sight of one collimation line is linked to the back sight of the next collimation line.
Stadia lines
Two short level lines equal distance above and below the levelling line in the telescope.
The distance between the stadias is read off the staff.
Distance between stadia lines
multiplied by 100 = distance from instrument to staff.

## Slide 6: Setting Up The Tripod
CONSTRUCTION LEVELLING
17/06/2019
>>FACULTY OF TECHNOLOGY AND BUILT ENVIRONMENT
Unitec School of Construction and Infrastructure

## Slide 7: Remember Our Setting Up?
Push two legs of the tripod firmly into the ground.
Get tripod head approximately level and push third leg into the ground. Do not set the tripod too low!
If the tripod is set on a steep slope, two of the legs must be secured in the ground roughly
at the same height on the downhill side of the instrument.
The remaining leg is secured to the uphill side. Adjust the remaining leg to level the tripod
head by sliding leg adjustment.

## Slide 8
Remember Our Level?

## Slide 9: Remember Our Bubble and Screw Adjustment?
Attach the levelling instrument firmly to the tripod head. If the setting up bubble is circular, the bubble must be in the centre of the ring.
Move the bubble towards the centre direction by using screws 1 and 2 to level the bubble.
Move the third screw to centralise the bubble. Once the bubble is centralised, check to ensure the instrument is levelled by rotating the instrument at 180 and 360. If the bubble remains within the circle after each rotation then the instrument is correctly set.
(Note: not necessary for automatic levels)

## Slide 10
The Levelling Staff

## Slide 11: Levelling and Booking
Levelling Staff
Standard staffs are 3 metres, 4 metres, or 5 metres long, they fold or telescope down to about1200 mm, have a reading face at least 38 mm wide.
The staff is graduated in 10mm increments with alternating black and red figures per metre on a white staff.
Reading the staff to the graduation will give 0.01m accuracy.
If three decimal places of accuracy are needed, it has to be estimated.

## Slide 12: Taking a Reading
17/06/2019
>>FACULTY OF TECHNOLOGY AND BUILT ENVIRONMENT
Unitec School of Construction and Infrastructure

## Slide 13
Levelling and Booking

## Slide 14: Taking a Reading
The method of taking readings differs slightly with the type of instrument being used; However the instrument must be set up level.
The staff holder must hold the staff on the mark or peg. Ensure the staff is plumb and facing the instrument.
Ensure the staff is visible for the instrument to focus on. If the parallax has been eliminated, the black hair line will be sharply outlined against the staff.
To remove the parallax you will need to focus the cross hairs separately. This is done by having the background out of focus and then focusing the cross hairs against the out of focus background.

## Slide 15: Note.
STADIA LINES (view through telescope)
The degree of accuracy for stadia is 100 mm in 30 metres
EXAMPLE Stadia lines read 2.043(top) and 1.872(bottom) Difference = .171 That is, 171 x 100= 17100mm or 17.1m

## Slide 16: Booking and Reducing the Readings
• E17x/0a6/m2019ple shown over
Utnhiteec Schpooal ogf Ceonstruction and
Infrastructure
Booking and reducing the readings by Rise & Fall method.
Rule up a level sheet as shown.
BS = Back; Site IS = Intermediate Site; FS = Forward Site; Rise
= Rising? Fall = Falling?
RL = Reduced Level New Level of FS; Dist = Distance by Measuring Tape IS to FS Staff;
Remarks
Record BS, IS, FS, readings in the correct columns as you take the readings.
When readings are complete, calculate rises & falls
Calculate reduced levels and Check your calculations.
BS | IS | FS | Rise | Fall | RL | Dist | Remarks

## Slide 17: EXAMPLE
The sketch below shows the spot levels taken on a sloping site.
Back Sight
Forward Sight
Intermediate Sight
Intermediate Sight
Back Sight
Forward Sight
Back Sight
Intermediate Sight
Chainman (Staff Holder), stays at D during Change of Station for Resighting onto D, E and F.

## Slide 18
Unitec School of Construction and
Infrastructure
Taking a Reading
Chainman (Staff Holder), stays at F during Change of Station for Resighting onto F and G.
17/06/2019

## Slide 19: To calculate the rise or fall
Subtract the second reading from the first reading.
If the answer is positive, there is a rise.
If the answer is negative (-), there is a fall.
A to B: 4.180- 3.090 = 1.090(rise) B to C3: .090- 1.980= 1.110(rise)
C to D: 1 .980- 0.270=1.710 (rise)
D to E: 2.240- 1.820= 0.420 (rise)
E to F: 1.820- 3.170=- 1.350 (fall)
F to G: 0.310- 3.590=- 3.280 (fall)
Calculate the reduced level (RL) by adding rises and deducting falls from the previous RL reading.

## Slide 20: Checking Rise and Fall
To check on rise and fall method
Add back sights, add fore sights and Take total of fore sights from total of back sights (or vice versa).
Add rises, add falls and Take total of rises from total of falls (or vice versa).
Subtract last reduced level reading from first reduced level reading (or vice versa).
Answers from (a) (b) and (c) should be equal.

## Slide 21: Contour Plans
17/06/2019
>>FACULTY OF TECHNOLOGY AND BUILT ENVIRONMENT
Unitec School of Construction and Infrastructure
Establishing contours is most suited for an overview of the whole site for things such as the overland flow of water or gradients of proposed driveways

## Slide 22: Contours Gradient
Gradient formula
Gradient = AB =
vertical interval BC horizontal equivalent
e.g. The gradient of the slope between (i) and (ii)
5/28 = 1/5.6 Therefore for every 5.600mtrs there is a 1mtr rise.

## Slide 23: Reading Contours
As above the contours shown describe the form of the land
Direction A would be a descending ridge with steep sides
Direction B would be a steep descending gulley
Direction C is a gradual descent with a rounded surface The graduations above are in 5 meter stages. This would be impractical for gentle slope, such as a residential section. On gentle sloped site it would be more practical to have the intervals at 0.500m intervals

## Slide 24: Formula for dividing grid points using say 1 contour for the general rise and fall
From the reduced levels establish where the graduations will land. On the grid you have the reduced levels recorded and where one of the RL’s is greater than the graduation means there will be a contour line or lines plotted between them.

## Slide 25: For Example 1 Method of Contouring
Using the Grid Method Calculate where a 0.500 interval is between 55.604 and 55.434 by subtracting one from the other 55.604
- 55.434 = 170.
Divide the grid into 17 parts (scaled = 10mm rises). Therefore 55.434 + 7 parts will be where 55.500approx crosses the line.
55.604 RL
55.434
=170
17
Parts
= 10
mm Rises

## Slide 26: For Example – Another Formula for dividing between two grid points.
Otherwise, Firstly Establish the graduations. The graduations could be .250 or .500m for small sites like residential properties and small lifestyle blocks, 1-10m for larger areas or very steep sites.

## Slide 27: Dividing Between 2 Grid Points
From the reduced levels establish where the graduations will land. On the grid you have the
reduced levels recorded and where one of the RL’s is greater than the graduation means there
will be a contour line or lines plotted between them.
Below is an example:
Firstly grid the section as shown adjacent >

## Slide 28: Where to put the Contour Lines?
Let’s say the contour lines are at 0.250 intervals. This means the contours will be at …50.000, 50.250, 50.500, 50.750, 51.000… etc.
Take note that they could also be below 50.000, like
49.500 or 48.750. Knowing this now look at the measurements and assess where a contour line will be as in the diagram below.

## Slide 29: Plotting the Contours
m
Secondly, once you have shot the heights, record the on the grid references as adjacent >.
Thirdly, start to plot the contour lines between the gridlines. You can use Scaled Drawing Methods

## Slide 30: How to calculate the position of the contour line by Scaled Drawing Method
Take the two levels where you know a contour line is going to intersect and subtract one from the other
50.307 – 50.127 = 180
Divide 180 by 20 (We use 20 because the scaled drawing method graphic divider has 20 parts) = 9 Therefore each of
the 20 parts represents 9mm.
Unitec School of Construction and
Infrastructure

## Slide 31
Take the higher level and subtract 50.250
50.307 – 50.250 = 57mm
Divide 57 by the 9mm obtained above.
= 6.3 (round down or up). Therefore, come down 6 units from 50.307 and this is where 50.250 intersects Elevation
Or - Now we can find the location of the 50.250 contour line by using the Same Scaled Drawing Method
and plan view of contour line.
Unitec School of Construction and
Infrastructure

## Slide 32: More Than One Contour Per Grid
17/06/2019
>>FACULTY OF TECHNOLOGY AND BUILT ENVIRONMENT
Unitec School of Construction and Infrastructure

## Slide 33: What to do if more than one contour line is between the plotted levels on the grid?
Find the difference between
50.364 and 51.581
• = 1217
Divide the answer by 20(We use 20 because the graphic divider has 20 parts)
• = 60.85
Therefore each of the 20 parts represents 60.85mm
Now we can find the location of the 51.500 contour line

## Slide 34: What to do if more than one contour line is between the plotted levels on the grid?
Take the higher level and subtract 51.500
51.581 – 51.500 = 81
Divide 81 by 60.85
= 1.33 (round up or down)
Therefore, come down 1 unit
from 51.581 and this is where
51.500 intersects
Then divide 250 by 60.85
= 4.1 (round up or down) Therefore mark every 4 units along for the 250 interval

## Slide 35: Grid Plan with the Contours Drawn at
The Finished Contour Plan
0.250 Metre Heights

## Slide 36: The End
Setting Up of the Levelling Instrument